## ICL Application Note 	No. 00013

# Configuring Freewave Radio for use with Multiple Repeaters

This document will walk you through the process of using more than one repeater with your Freewave Radios.

### Configuring the Radio

Connect your Radio via the diagnostic port and open HyperTerminal. The default settings will be a baud of 19200 and no flow control. Once you are connected please tap the + key 3 times in quick succession to bring up the main Menu.

Press 5 to get into the “Multipoint Parameters” and type C to get into the Subnet ID choices. From this menu set the Transmit and Receive SubnetID’s for your device.

*The subnet ID’s MUST match. IE: If the master has a Transmit ID of 1 then the first repeaters Received ID needs to be set to 1. Please see the diagram below for more information.

The menu will prompt you to change both of these in succession. Once you have changed these you can proceed to the next unit. You will need to change each device to the settings listed in the above diagram.

This will allow you to use two repeaters in your system.

Contact Information

Toll Free		(800) 888-1893

Local			(530) 888-1800

Fax			(530) 888-7017

Email			support@iclinks.com

Web			http://www.iclinks.com

Mail			12840 Earhart Avenue ( Auburn, CA USA 95602