## ICL Application Note 	No. 00014

# Importing from ISaGRAF PIA

This document will walk you though importing an ISaGRAF PIA file.

### Instructions:

- Open ISaGRAF Projects from the Start Menu

- Click on “Tools” and “Archive” then select “Projects”

- Browse to your PIA file and select it

- Click on “Restore”

- Double click on the newly imported PIA file

- Click OK to any errors that you receive

- Change all registers to Internal

- Save the changes and open SCADABuilder

- Create a new Node and tell it to “Use an existing ISaGRAF Project”

- You will need to do a search for the “nodename.pgm” where nodename.pgm is the name of the PIA file that you imported. When you find the PGM file right-click on it and select “Open containing Folder”. Use this folder as the import directory in SCADABuilder.

### Summary

The information listed in this file will allow you import from an ISaGRAF PIA file into SCADABuilder. Once you have imported your PIA file you can re-map the registers in the I/O configuration.

Contact Information

Toll Free		(800) 888-1893

Local			(530) 888-1800

Fax			(530) 888-7017

Email			support@iclinks.com

Web			http://www.iclinks.com

Mail			12840 Earhart Avenue ( Auburn, CA USA 95602