## ICL Application Note 	No. 00015

# Importing new Libraries into ISaGRAF

This document will walk you through importing any new libraries that you have into the ISaGRAF application. Please follow the instructions listed below.

- In order to import the new libraries into ISaGRAF we need to first launch the libraries program. Click on your Start Menu and go to the ISaGRAF folder. Click on “Libraries”.

- Once the Libraries program is running you will see the following screen:

- Click On “Tools” and select “Archive”.

- Browse to the location of the library files that need to be imported.

- Then click “Restore”.

- You should now have a window that looks like the one below:

- Highlight one of the library files and Click on “Edit” and select “Source Code” (You will need to do this for both Library files).

- Once the ISaGRAF program starts you can click on the “Verify program” option from the toolbar.

- You should see the following screen.

* Remember to go back and verify any other library files that you need to import.

Contact Information

Toll Free		(800) 888-1893

Local			(530) 888-1800

Fax			(530) 888-7017

Email			support@iclinks.com

Web			http://www.iclinks.com

Mail			12840 Earhart Avenue ( Auburn, CA USA 95602