## ICL Application Note 	No. 00021

# Configuring Modbus TCP Slave

This document will walk you through configuring the Modbus TCP Slave protocol on your Etherlogic Controller via the Ethernet port.

### Enable TCP/IP

Open your SCADABuilder project and go into the Node Options. Click on the TCP/IP tab and check the box next to “Enable TCP/IP”. Type in the IP address that you want to use and any other information necessary for your network

### Creating the Network Session

Now it’s time to create the Network Session. You can do this by going to the “setup” menu and selecting “Network Sessions…” or simply click ont eh NetSessions button in the dialog above.

You will see a screen that is similar to the following:

Summary

After you have completed the steps in this document you should have a controller that is configured to talk Modbus TCP Slave over Ethernet.  This is a configuration for “Standard Modbus” where the register index is used as the Modbus register address in the following formats:

0x<Register address>		read/write Booleans

1x<Register address>		read only Booleans

3x<Register address>		read only Integers

4x<Register address>		read/write Integers

Please let us know if you have any questions or comments about this document.

Contact Information

Toll Free		(800) 888-1893

Local			(530) 888-1800

Fax			(530) 888-7017

Email			support@iclinks.com

Web			http://www.iclinks.com

Mail			12840 Earhart Avenue ( Auburn, CA USA 95602