## ICL Application Note 	No. 00029

# Sending an Email from a GSM Connection

This walkthrough will allow you to create and send an email through a GSM PPP connection on your Etherlogic controller. In order for this to work properly you need to be sure that your Etherlogic has the cellular modem option installed. You also will need to know the carrier that you plan to use and any additional connection information that they may require to connect.

### Enable the Modem Port

- When you open your SCADABuilder project, be sure to name the Modem port in your Network Ports screen to ensure that it is enabled.

- Make sure that your baud rate is set to 38400

### Configuring TCP/IP

- Click on TCP/IP and the following window will appear:

- Check the “Enable serial TCP/IP” check box and check the “Enable Client Services” box.

- Make sure that “Obtain domain name servers” is checked.

- Fill out the remaining sections with your information and click OK.

- Click OK again on the “Network Ports” Box to close the window.

### Creating a Trigger

- In order to create a Trigger you need to Double-click on the Trigger section of SCADABuilder

- Once you double-click the Trigger you will get a dialogue box asking for the name. Go ahead and name the trigger.

- Set the Trigger parameters to match your system setup.

- Click OK when you have completed the Trigger setup.

### Create a Network Session (Modem)

- Click on “Setup” and select “Network Session…” from the main menu.

### Dialup Setup

- Select your modem driver from the list provided in the lower section of this screen.

- If you are not using a carrier listed in this drop-down menu open your SCADABuilder folder from the C:\ drive and open the “Access” folder.

  - You will see a file called “ModemDriver.ini”. If you open this file you will see a section that says “//Specific argument for communicating with T-Mobile (Your Carrier May Differ).”

    - You will need to change to reflect your carriers’ specifications.

### Email Address

- On the “Misc” tab please enter your email address in the “Account/Domain name:” box.

### Creating the Email

- Click on the “Email” button located in the lower right-hand corner of the window

- Fill out the necessary fields on the “Compose” window and be sure to set your Triggers in the Triggers tab.

- Email Body should contain the register and any information that you would like the entry to contain.

### Summary

Once you have completed these steps you will be able to send an email from your GSM connection through the internet onto a receiving PC.

Contact Information

Toll Free		(800) 888-1893

Local			(530) 888-1800

Fax			(530) 888-7017

Email			support@iclinks.com

Web			http://www.iclinks.com

Mail			12840 Earhart Avenue ( Auburn, CA USA 95602