## ICL Application Note 	No. 00036

# Formatting your Controller
This needs to be completed when you are no longer able to delete files from the controller

### Open a Terminal Window

- In order to perform the format you need to open a terminal window. Once you have opened the window, reboot the controller and tap the ESC key until it displays a DOS Prompt.  If it goes past “Starting ROM-DOS” press reset again and start over.

### Performing the Format

- At the C:\Prompt type in “fxfmt 80” and press ENTER. You will see the following:

- Type “Y” to proceed with the format.

- When the format is complete you will see something like the following screen:

- At this point you need to push the reset button on your controller and let it reboot:

- Once the controller reboots to this prompt you are ready to Send a complete setup to the controller.

  - From the SCADABuilder window click on “Target” and select “Send Complete Controller Setup”

### Summary

The controller is now ready to be downloaded to. You should no longer be receiving the error when attempting to download or delete files from the controller.

Contact Information

Toll Free		(800) 888-1893

Local			(530) 888-1800

Fax			(530) 888-7017

Email			support@iclinks.com

Web			http://www.iclinks.com

Mail			12840 Earhart Avenue ( Auburn, CA USA 95602