## ICL Application Note 	No. 00037

# Retrieving Files from your Etherlogic Controller

This document will walk you through retrieving files via FTP from your Etherlogic controller using your ScadaWorks software.

### Accessing the File Transfer Window

- Open ScadaBuilder and go to the Tools Menu. Once there click on “File Transfer”

### File Transfer Window

- Once on the file transfer window you will see a setup that looks like you’re used to seeing in an FTP client.

  - One the left half of the screen is your Local PC side

  - On the right half of the screen you will see the remote host.

    - Note: The Status dialogue box on the top of this screen has important information regarding the status of the file transfer.

### Configuring your Filters

- Below the Status dialogue box is the “Filter:” settings. Make sure that the files you are trying to retrieve extensions are on this list.

  - If they do not show up on this list you will not see them in the list window

  - Pull this menu down to select “All Files”

### Starting the Transfer

- Highlight the file you want to transfer from the remote side and press the “<<” button.

- This starts the transfer

### Summary

You have now successfully transferred a file from your Etherlogic controller onto your Desktop or Laptop PC. You will need to reset the unit or press  on the ScadaBuilder Main Page to restart the node.

Contact Information

Toll Free		(800) 888-1893

Local			(530) 888-1800

Fax			(530) 888-7017

Email			support@iclinks.com

Web			http://www.iclinks.com

Mail			12840 Earhart Avenue ( Auburn, CA USA 95602