## ICL Application Note 	No. 00049

Using ScadaWorks with Windows Vista SP1

*This document applies to Scadabuilder/Works 3.1 and prior.

*You must complete the Service Pack 1 Update before ScadaWorks will work properly.

In order to do a complete controller setup through ScadaWorks you must follow the steps outlined below:

(If you are only using the ScadaBuilder package please disregard these steps)

Complete Controller Setup

- Open ScadaWorks and open the project that you want to download to your controller:

- Next, click on the Target Menu and select “Clean Target”. This will clean any existing program from the controller:

- Once the “Clean Target” operation is completed go back to the Target Menu and select “Send
ISaGRAF Runtime Kernel”. This will send the current version of the kernel that you are using to the controller:

- Once the Kernel transfers you will next need to Send Sockets to the controller so that it can communicate via Ethernet (FTP/HTTP etc.). You can do this by clicking on “Target” and selecting “Send Sockets…”:

- At this point you have sent most of the information needed to download your project.

* If you use Voice in your project (VUI’s, Dialers, Etc.) you will need to also hit the “Generator

Voice…” as Windows Vista has a different set of voice drivers than Windows XP (at this time they

are not compatible with one another).

Downloading your Project

At this point you have successfully transferred the Kernel, the Socket configuration, regenerated and sent the Voice files that need to be on the controller. From here on out you can perform regular downloads like you were able to with Windows XP. Please refer to Application Note #45 for information on how to Download your project:

Downloading via FTP

Because of the changes made by Microsoft in this latest version of Windows you will need to populate the “Internet IP address (WAN):” field in the Node Settings on the Ethernet/Serial IP tab:

Summary

This should get you through some of the quirks of downloading through a Windows Vista SP1 Operating System with the least amount of hassle.

Contact Information

Toll Free		(800) 888-1893

Local			(530) 888-1800

Fax			(530) 888-7017

Email			support@iclinks.com

Web			http://www.iclinks.com

Mail			12840 Earhart Avenue ( Auburn, CA USA 95602