## ICL Application Note 	No. 00051

Modem Driver Reference v1.00

ScadaBuilder includes a powerful scripting language that allows you to create custom modem drivers for use with nearly any modem device, including standard dialup and cellular data modems.  This document lists the available commands you can use to create a custom modem driver for your application.

The modem driver scripts are stored in the ‘ModemDriver.ini’ file located off the ScadaBuilder installation directory, ‘Access’ subdirectory in a file called ‘ModemDriver.ini’ (typically C:\Program Files\ICL\ScadaBuilder\Access\ModemDriver.ini).  You can edit this file using the windows notepad application.

You can always download the current release of the ModemDriver.ini file from the support section of http://www.iclinks.com.

# Parameters Formats

##### Comment

//	Start line with “//” to insert a comment

##### Driver Name

[(name)] 	(name) = name of modem driver

##### Driver Version

VERS = (x.xx)	(x.xx) = modem driver version number

##### Driver Section

SECT = (list)	(list) = MONITOR | CONNECT | DISCONNECT

##### Modem Command

CMD= (str)	(str) = command string (may insert any token into string)

#### Modem Response

RSP = (wait) (str)	(wait) = time to wait for response in seconds

(str) = response string (may insert any token into string)

##### LED Control

LED = (state)	(state) = ON | OFF

##### Flush Receiver

FLUSH                	(no parameter values)

##### Inter-Character Delay

PACE = (time)	(time) = time between characters sent to modem in milliseconds

##### Operation Delay

DELAY = (time)	(time) = time to wait before processing the next operation in milliseconds

##### Baud Rate

BAUD = (list)	(list) = 300 | 1200 | 2400 | 4800 | 9600 | 19200 | 38400 | 57600 | 115200

##### Data Bits

DATA = (num)	(num) = number of data bit to set for port

##### Stop Bits

STOP = (num)	(num) = number of stop bits to set for port

##### Parity

PARITY = (list)	(list) = NONE | EVEN | ODD | MARK | SPACE | MARK_9 | SPACE_9

##### Carrier Detect

CD = (wait) [state]	(wait) = time to wait for the carrier detect state in milliseconds

[state] = ON | OFF (optional, default is ON)

##### Clear To Send

CTS = (wait) [state]	(wait) = time to wait for the clear-to-send state in milliseconds

[state] = ON | OFF (optional, default is ON)

##### Data Set Ready

DSR = (wait) [state]	(wait) = time to wait for the data-set-ready state in milliseconds

[state] = ON | OFF (optional, default is ON)

##### Ring Indicator

RI = (wait) [state]	(wait) = time to wait for the ring indicator state in milliseconds

[state] = ON | OFF (optional, default is ON)

##### Data Terminal Ready

DTR = (state)	(state) = ON | OFF

##### Ready To Send

RTS = (state)	(state) = ON | OFF

NOTES: The parameters above that use a (state) value may also use TRUE | FALSE | 1 |  0 for the value.

# Tokens

Tokens may be insert into the parameter values where specified.

<BAUDRATE>	NetPort baud rate: CMD, RSP, BAUD

<DATABITS>	NetPort data bits: CMD, RSP, DATA

<STOPBITS>	NetPort stop bits: CMD, RSP, STOP

<PARITY>	NetPort parity: CMD, RSP, PARITY

<DCEIPADDR>	NetPort PPP Client Gateway: CMD, RSP

<CONNTIMEOUT>	NetSession connect timeout: CMD, RSP, PACE, DELAY, CD, CTS, DSR, RI

<PHONENUM>	NetSession phone number (first numeric): CMD, RSP

Contact Information

Toll Free		(800) 888-1893

Local			(530) 888-1800

Fax			(530) 888-7017

Email			support@iclinks.com

Web			http://www.iclinks.com

Mail			12840 Earhart Avenue ( Auburn, CA USA 95602