## ICL Application Note 	No. 00052

# Complete Controller Setup via FTP

This document will walk you through a Complete Controller Setup using FTP. This can be useful if you need to upgrade your version of ScadaWorks and have multiple units in the field and can not easily connect via a serial connection.

*You must have FTP enabled for this procedure to work.

### Archive and Restore your Project

Before we begin we need to archive your project so that we can import it into the new version of ScadaWorks that you will be using. More information on this procedure can be found in Application Note #00026 (Archiving a Project) and #00027 (Restoring a Project).

### Performing the Complete Controller Setup Remotely via FTP

### Sending the Kernel

- We will start by updating the Runtime Kernel. You can do this by clicking on the Target menu and selecting “Send ISaGRAF Runtime Kernel”:

- When prompted to use FTP click YES:

- You will see the following screen during the transfer:

### Sending Sockets Configuration

- Once you have completed sending the Runtime Kernel to the controller you can go ahead to transfer the socket configuration to the unit. Do this by clicking on the Target menu and selecting “Send Sockets…”:

- When prompted to use FTP click YES:

- You will see the following screen during the transfer:

### Sending the Startup Configuration

- Finally, in order to send the project information to the controller and reboot it we need to go back to the Target menu and select “Send Startup Config and Start…”:

- When prompted to use FTP click YES:

- You will see the following screen during the transfer:

### Summary

Once this step completes your controller will have the newest Runtime Kernel and Socket Configuration for the new version of ScadaWorks. You will need to do this procedure every time you update ScadaWorks and need to remotely update any of your controllers.

Contact Information

Toll Free		(800) 888-1893

Local			(530) 888-1800

Fax			(530) 888-7017

Email			support@iclinks.com

Web			http://www.iclinks.com

Mail			12840 Earhart Avenue ( Auburn, CA USA 95602